Arduino Development Workshop
Brad Kelly
Matt Plavcan

---
Second in a Series
1. Getting Started With Arduino
2. Arduino Development Workshop
3. Advanced Arduino Workshop

---
Slides Available Online
https://github.com/bradakelly

---
Learning Objectives
- Understand digital circuit wiring basics
- Be able to read simple schematics
- Be able to add external devices to an Arduino
- Know how to structure Arduino sketches
- Learn basic Arduino debugging techniques
[Speaker Notes: 3 min]

---
Test Your Arduino: Load Blink Sketch!
[Speaker Notes: 1 min (no troubleshooting) 5 min (with troubleshooting)]

---
Control LED with Button
Sketch:
   Examples → 02.Digital → Button
Connect circuit as shown:
Why are the resistors needed?

---
Circuit Basics
Circuits have a current
    (flow of electrons)
Resistance limits the current
     (Higher resistance = lower current)

---
Digital Circuits Are Still Circuits
LEDs have some resistance, can be used with direct connection for simple configurations
For reliable designs, need resistors to avoid burning out Arduino outputs

---
Highs and Lows of Digital Circuits
Two different ways to connect an LED to an Arduino digital output:
Left: “HIGH“ voltage from Arduino turns on
        LED (Power flows from Arduino)
        (okay for single simple LED)
Right: “LOW“ voltage from Arduino turns on
        LED (Power flows into Arduino)
        (preferred for high-current applications)

---
Ups and Downs of Digital Circuits
An Arduino input pin can be:
“HIGH“ (positive voltage)
“LOW“ (grounded)
When an input is disconnected,
it can float to either value!

---
Ups and Downs of Digital Circuits
Two different ways to connect a button to an Arduino digital input:
Left: Pressing button results in “HIGH“ value
        for input
(active high)
Right: Pressing button results in “LOW“ value
        for input
 (active low)

---
Active HIGH Input
if (digitalRead(pin) == HIGH) {
  some_action();
}

---
Active LOW Input
if (digitalRead(pin) == LOW) {
  some_action();
}

---
Analog Inputs
Arduinos support six analog input pins (A0-A5)
Inputs voltages are between 0v and 5v (or 3.3v)
Analog inputs return a value between 0 and 1023
Read analog inputs using analogRead()

---
Analog Input
int input_value = analogRead(pin)
if(input_value > THRESHOLD) {
  some_action();
}

---
Schematic Symbols
Power
Ground
Diode
Light-Emitting
Diode (LED)
Pushbutton
(Normally Open)
Switch
(Normally Open)
Resistor
Variable Resistor
(Potentiometer)

---
Want to Connect Other Stuff?
Most inputs can be reduced to a digital or analog signal:
- All require pullup/down resistors
- Use of relays or transistors to make inputs safe for Arduino inputs
  (outside scope of this course)
- HOWEVER: Most shields or integrated devices handle this for you.

---
Using SeeedStudio’s Grove Shield
Disconnect Arduino from power
Connect Grove shield
(align pins carefully and press gently)
Attach the RGB LCD Display to the I2C bus connection
(pronounced “eye-squared-see” bus)
Connect Arduino power --> Display should illuminate

---
Downloading New Libraries and Examples

---
Open Example LCD Sketch
2. File → Examples → Grove-LCD_RGB_Backlight → Hello World
3. Run sketch and see "hello world" on display
4. Connect button and make it display
   a different message when button pressed
if (digitalRead(pin)
   == HIGH) {
   ...
} else {
   ...
}

---
Load the Fade Sketch
Load the following sketch and run it:
File --> Examples --> Grove-LCD RGB Backlight --> Fade
2. A few interesting things in here:
- Functions
- For loops

---
Using Functions (C++ style)
One parameter (input):
- name is color
- type is unsigned char
The return type (output) is void
Could be any type:
- int
- char
- float
- String
- etc...
Three calls to function in loop()
void breath(unsigned char color)
{
   ...
}
void loop()
{
   breath(REG_RED);
   breath(REG_GREEN);
   breath(REG_BLUE);
}

---
Other "flow control" Structures by Example
2. Look at the for loops:
7. Let's add some debug messages to see what is going on ...
   for (<do before loop>; <loop if true>; <do after each loop>)
   {
       some_repeating_action();
    }

---
Debug using Serial.print
1. There is a debug console you can print to:
2. Add this to the setup() function:
      Serial.begin(9600);
4. Add this to loop() function:
      Serial.write("Breathing color %c\n");
6. Click upper right icon before running
7. Add a few more useful print statements

---
Wipe Text Left to Right
Go back to “Hello world“ sketch
Make the display "wipe“ from left to right
    (One character appears at a time)
Will require:
- String variable:
- For loop over a string:
- Indexing into string:
   String str = "hello world";
    for(int i=0; i < str.length(); i++)
   { … }
   str[1] // get second letter

---
Wipe Text Left to Right
Go back to “Hello world“ sketch
Make the display "wipe“ from left to right
    (One character appears at a time)
Will require:
- String variable:
- For loop over a string:
- Indexing into string:

---
Variable Scope
1. Variables only exist in the "scope" they are defined
2. Scope is defined as a curly braced areas
4. Guideline:
5. With well formatted code,
   once editor "outdents" then all variables
   declared in that block go away

---
Variable Scope
1. Important:
2. loop() and setup() have a scope!
4. Use global variables to retain or
   pass information

---
Wipe with a Global Variable
Change your "wipe from left to right":
    Use a global variable to save the current position between calls to loop()
How:
  - Move loop variable to the top to be global and initialize
  - Increment loop varaible at bottom of loop
  - Set value to 0 again if value > max count value

---
Open Experimentation
1. Now lets have some fun!
2. Grab any input sensor
3. Make the LCD display show something about it
4. NOTE: You may have to add new libraries:
       Sketch --> Include Library --> Manage Libraries
6. When ready, try other output devices

---
fin
brad.a.kelly@gmail.com
mwplavcan@gmail.com